## Slide 1: MCQ Engineering Chemistry
Chemical Engineering Department
Made by: Eng.
Chapter 5

## Slide 2: Summary
I. Define
1-Oxidation : loss of electron (s) by a species.
2- reduction : gain of electron(s).
3- oxidizing agent : Oxidizing Agent causes oxidation & is reduced.
4- reducing agent : Reducing Agent causes reduction & is oxidized.
5- Estandard electrode potential ( : it is the electrode potential measured at 1 M solution concentration and 1cm ² and all gases are at 1atm at C.
6- Nernst equation:
7- Corrosion : the transformation of a metal from elemental to the combined state.

## Slide 3: Summary
II. Discuss
A-Explain different corrosion forms?
1- Uniform corrosion (general corrosion)
- The most common type
- Due to chemical or electrochemical reaction
- Happen over the surface of metal
2-Galvanic corrosion
- happen between two metal contacts with each other
- Metal with less potential is the anode (corrode), the metal with higher potential is the cathode
- Like cupper with iron.
3- Pitting corrosion
- Very dangerous and grows with the gravity
- Like all metals subjected to high velocity liquids, cupper and brass tubes
4-Stress corrosion
- its the growth of crack formation in a corrosive environment.
- This form of corrosion is particularly dangerous because it may not occur under a particular set of conditions until there is an applied stress.

## Slide 4: Summary
State different methods for corrosion prevention?
  1-Environmental Modifications
  2-Metal Selection and Surface Conditions
  3-Cathodic Protection
  4-Corrosion Inhibitors
  5-Coating
  6-Plating

## Slide 5
Explain different methods of cathodic protection?
  1-sacrificial anode, uses metal anodes, introduced to the electrolytic environment, to sacrifice themselves (corrode) in order to protect the cathode.
  2-impressed current protection.
What is the importance of corrosion inhibitor?
  Inhibitors can work by adsorbing themselves on the metal's surface and forming a protective film.The inhibitors process is slowing corrosion process

## Slide 6: Choose the correct answer:
1- in an electrolytic cell the electrode at which the electrons enter the solution is called the __ ; the chemical change that occurs at this electrode is called ___.
  (a) anode, oxidation
  (b) anode, reduction
  (c) cathode, oxidation
  (d) cathode, reduction
  (e) cannot tell unless we know the species being oxidized and reduced.
Answer d

## Slide 7: Choose the correct answer:
2- Which of the following methods is not used for the prevention of corrosion?
  a) greasing
  b) painting
  c) plating
  d) Heating
Answer: b

## Slide 8: Choose the correct answer:
3- Corrosion can be prevented by
a) alloying
b) tinning
c) galvanizing
d) all of the above
Answer: (d)

## Slide 9: Choose the correct answer:
4- Galvanic cells are also named as:
a) electrolytic cells
b) battery cells
c) daniel cells
d) john cells
Answer: a
Explanation: Galvanic cells, also known as voltaic cells, are electrochemical cells in which spontaneous oxidation-reduction reactions produce electrical energy.

## Slide 10: Choose the correct answer:
5- Galvanization is a method to
a) protect the iron metal from corrosion
b) extract iron from its ore
c) protect food from rancidity
d) improve the ductility property of the metal
Answer: a
Explanation: Galvanisation is a method of protecting iron and steel from rusting by coating them with zinc.

## Slide 11: Choose the correct answer:
6- Corrosion between the dissimilar metals is called as ____
a) Galvanic corrosion
b) Dry corrosion
c) Oxidation corrosion
d) Concentration cell corrosion
Answer: a
Explanation: Corrosion between the dissimilar metals is called as the galvanic corrosion. Dry corrosion also called as the chemical corrosion.

## Slide 12: Choose the correct answer:
7- Corrosion due to the formation of cavities around the metal is called as the _____
a) Pitting corrosion
b) Soil corrosion
c) Water line corrosion
d) Galvanic corrosion
Answer: a
Explanation: Corrosion due to the formation of cavities around the metal is called as the pitting corrosion. Corrosion between the dissimiliar metals is called galvanic corrosion.

## Slide 13: Choose the correct answer:
8- The process of deterioration of a metal due to unwanted chemical or electrochemical interaction of the metal with its environment is called _____:
a) Electrolysis
b) Electrodialysis
c) Corrosion
d) Deposition
Answer: c
Explanation: The process of deterioration of a metal due to unwanted chemical or electrochemical interaction of the metal with its environment is called corrosion. It is a natural process, which converts a refined metal to a more stable form, such as its oxide, hydroxide, or sulfide.

## Slide 14: Choose the correct answer:
9- On anode __ reaction occurs :
a) Oxidation
b) Reduction
c) Redox
d) None of above
Answer: a
Explanation: The reaction at the anode is oxidation and that at the cathode is reduction.

## Slide 15: Choose the correct answer:
10- In Redox Reaction, electrons may be
Gained only
Lost only
Shared
Gained and lost
Answer: d

## Slide 16: Choose the correct answer:
11- Electrochemical cell is achieved by connecting two
a) ions
b) electrodes
c) half cell
d) non of above
ANSWER: c

## Slide 17: Choose the correct answer:
12- Electromotive force is equal to
a) E cathode – E anode
b) E anode – E cathode
C) E -
ANSWER: a

## Slide 18
13- A galvanic cell with a measured standard cell potential of 0.27 V is constructed using two beakers connected by a salt bridge. One beaker contains a strip of gallium metal immersed in a 1 M solution of GaCl3, and the other contains a piece of nickel immersed in a 1 M solution of NiCl2. The half-reactions that occur when the compartments are connected are as follows:
cathode: Ni2+(aq) + 2e− → Ni(s)
anode: Ga(s) → Ga3+(aq) + 3e−
If the potential for the oxidation of Ga to Ga3+ is 0.55 V under standard conditions, what is the potential for the oxidation of Ni to Ni2+?
a) E°cathode = −0.28 V
b) E°cathode = −0.46 V
c) E°anode = −0.28 V
Answer: a
Explanation: A We have been given the potential for the oxidation of Ga to Ga3+ under standard conditions, but to report the standard electrode potential, we must reverse the sign. For the reduction reaction Ga3+(aq) + 3e− → Ga(s), E°anode = −0.55 V..
E°cell = E°cathode − E°anode
0.27 V = E°cathode − (−0.55 V)
E°cathode = −0.28 V

## Slide 19: Choose the correct answer:
14- The following electrochemical cell is made:
Cu(s)|Cu2+(aq, 0.1 M)||I‐ (aq, 0.1 M)|I2(s)|C(s)
The cell potential was measured and found to be 0.279 V. Calculate E°cell
a ) 0.321 V
b) 0.290 V
c ) 0.190 V
ANSWER: c
Explanation: Ecell = E°cell –(0.0592/2)log{[Cu2+][I­ ]2} or
E°cell = Ecell + (0.0592/2)log{[Cu2+][I­ ]2} = 0.279 V + (0.0592/2)log(0.1)3
E°cell = 0.279 V – 0.0888 V = 0.190 V

## Slide 20: Thank you
Any questions?